## Slide 1: Timing is everything
Design and Analysis of Operations Research Methods for Optimization of Rail Network Traffic

## Slide 2: Setting
Train traffic on a single line
Existing schedule of trains
Notes: More about regional, but long distance lines (regional traffic, lines between cities)

## Slide 3: Example Train Network

## Slide 4
Signal blocks
Station blocks
Switch blocks
Notes: Gleise
Abbildung nicht Maßstabsgetreu!

## Slide 5: Motivation (delivered by DB)
Every day 23505 trains are traveling on the german railway network
1109 million km travelled
1,203 billion* passengers per year
3,9 million passengers per day
A high potential for optimisiation!
Notes: \* english Billion = german Milliarden
Source: Deutsche Bahn Daten und Fakten 2021, https://www.deutschebahn.com/resource/blob/7537106/7d38dfcb4de528171002c09ae29ba705/DuF2021-data.pdf

## Slide 6: Goal
Is it possible to schedule new trains on an already busy train route?
If so, how?

## Slide 7: The ATP

## Slide 8: Additional Trainpath Problem (ATP)
Given
Block network graph , derived from real train network N
Existing and new trains R_ex and R_new
Timehorizon T
Arrival and departure times A_R_ex and D_R_ex for existing trains
Arrival and departure constraints bar(A)_R_new and bar(D)_R_new of new trains

## Slide 9: Story of the ATP
ATP is closely related to many other scheduling problems
Stems from Train Timetabling Problem

## Slide 10: ATP for our Example Network

## Slide 11
Signal blocks
Station blocks
Switch blocks
Notes: Gleise
Abbildung nicht Maßstabsgetreu!

## Slide 12
Signal blocks
Station blocks
Switch blocks
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 13
Signal blocks
Station blocks
Switch blocks
0
1
3
2
6
4
5_1
7
5_0
Blockgraph
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 14
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 15
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph
ATP:
Block network graph
Existing and new trains
Timehorizon T
Arrival and departure times
Arrival and departure constraints
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 16
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph G_N
Fast Trains
ICE 0
ATP:
Block network graph
Existing and new trains
Timehorizon T
Arrival and departure times
Arrival and departure constraints
Three Existing Trains
Slow Trains
RE 0
RE 1
and Three New Trains
ICE 1 (f1)
ICE 2 (f2)
RE 2 (s0)
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 17
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph G_N
ATP:
Block network graph
Existing and new trains
Timehorizon T
Arrival and departure times
Arrival and departure constraints
Time Horizon
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 18
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph G_N
ATP:
Block network graph
Existing and new trains
Timehorizon T
Arrival and departure times
Arrival and departure constraints
Arrival and Departure Times
Trains |  |  |  |  |  |  |  | 
 | A | D | A | D | A | D | A | D
ICE 0 | - | 1 | 4 | 5 | 10 | 20 | 23 | -
RE 0 | - | 11 | 16 | 18 | 26 | 30 | 33 | -
RE 1 | - | 31 | 36 | 38 | 46 | 50 | 53 | -
0
2
5_x
7
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 19
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph G_N
ATP:
Block network graph
Existing and new trains
Timehorizon T
Arrival and departure times
Arrival and departure constraints
Arrival and Departure Constraints
Trains |  |  |  |  |  |  |  | 
 | A | D | A | D | A | D | A | D
ICE 0 | - | 1 | 4 | 5 | 10 | 20 | 23 | -
RE 0 | - | 11 | 16 | 18 | 26 | 30 | 33 | -
RE 1 | - | 31 | 36 | 38 | 46 | 50 | 53 | -
RE 2 | - | 5 | 10 | 12 | 20 | 24 | 27 | -
ICE 1 | - | 15 | 18 | 19 | 24 | 34 | 37 | -
ICE 2 | - | 25 | 28 | 29 | 34 | 44 | 47 | -
0
2
5_x
7
Notes: TODO: Zeichnung und dann Graph überblenden?

## Slide 20: Two models

## Slide 21: Mixed Integer Program
“Simple“ model for ATP
Binary variables

## Slide 22: MIP Structure
Variables for
arrival and departure at each block
train order
block usage
Minimizing:
sum of deviations from (planned) arrival and departure times
Notes: TODO: Print MIP?

## Slide 23: Time-Expanded Network
Motivation: Algorithmic method vs “black box“ LP-solver
Idea:
  Construct copies of the network for each timestep
  Solve ATP by finding feasible paths
Finding feasible paths by deleting “blocked“ edges
Notes: Motivation
Idea
Algorithms
Parts of algorithms shown for the example

## Slide 24
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph G_N
Trains |  |  |  |  |  |  |  | 
 | A | D | A | D | A | D | A | D
ICE 0 | - | 1 | 4 | 5 | 10 | 20 | 23 | -
0
2
5_x
7

## Slide 25
Signal
Station
Switch
0
1
3
2
6
4
5_1
7
5_0
Blockgraph G_N

## Slide 26: Finding a Path
TEN can only insert one new train at once
Construct TEN for each new train
A feasible path in the TEN is a feasible train path (i.e. timetable)
  How to find such?

## Slide 27: Edge Deletion
Already running trains resemble paths in the TEN
Delete edges that are not usable for the new train
  Simple and
  Advanced edge deletion

## Slide 28
Advanced Edge Deletion
For all “artificial edges“:

## Slide 29
Advanced Edge Deletion
For all “artificial edges“:

## Slide 30
Simple Edge Deletion

## Slide 31: Storyboard (Summary of What and How)
Motivation
Goal
Train Timetabling
ATP
Two Models
MIP
TEN
Edge Deletion

## Slide 32: Programming a Framework

## Slide 33
Network
Generator
Feasibility
Check
Properties
Generated Network / Train Data
Network Data
Main Test Script
TEN
Network Data
New Timetable
MIP

## Slide 34
Main Test Script
TEN
iterative
Network Data
All new trains at once
MIP
global
MIP
iterative
One new train
at a time
One new train
at a time

## Slide 35: Results

## Slide 36: Solving the ATP
Test cases with different
  network size
  stations
  existing trains
  new trains
Blocks | Stations | Ex. Trains | New Trains
10 | 3 | 3 | 3
10 | 3 | 5 | 5
20 | 3 | 3 | 3
20 | 3 | 5 | 5
20 | 5 | 5 | 5
30 | 3 | 3 | 3
30 | 3 | 5 | 5
30 | 5 | 5 | 5
30 | 7 | 7 | 7
40 | 3 | 3 | 3
40 | 5 | 5 | 5
40 | 7 | 7 | 7
50 | 3 | 3 | 3
50 | 5 | 5 | 5
50 | 7 | 7 | 7
50 | 10 | 10 | 10

## Slide 37
Computational Results

## Slide 38: Conclusion

## Slide 39: Take Aways
Problem becomes increasingly harder for larger instances
Lots of potential for improvement
  MIP
  TEN

## Slide 40: What about our example network??

## Slide 42: Motivation
Every day 23505 trains are traveling on the german railway network
1109 million km travelled
1,203 billion* passengers per year
3,9 million passengers per day
A high potential for optimisiation!
Notes: \* english Billion = german Milliarden
Source: Deutsche Bahn Daten und Fakten 2021, https://www.deutschebahn.com/resource/blob/7537106/7d38dfcb4de528171002c09ae29ba705/DuF2021-data.pdf